## Slide 1: Balancing Efficiency and Flexibility
Cost of Abstractions in Embedded Systems Marcell Juhasz
Notes: Hello Everyone! I am Marcell Juhasz. Welcome to my presentation about the cost of abstractions in embedded systems.

## Slide 2
whoami
Marcell Juhasz
github.com/juhaszmarcell96
linkedin.com/in/juhaszmarcell
marcell.juhasz96@gmail.com
Zühlke Engineering (Austria) GmbH
Rivergate, Handelskai 92
1200, Vienna, Austria
wien@zuehlke.com
+43 1 205 11 6800

## Slide 3
Motivation
C is dominant in the embedded world
  direct interaction with hardware
  flexible
  robust
  efficient
Common opinions:
  C is as efficient as it gets
  abstraction = less efficient software
  C++ comes with inherent runtime overhead

## Slide 4
Overview
Hardware Abstraction Layer
Encapsulation
Inheritance
Polymorphism
+
Template Metaprogramming
Concepts
Constant Expressions
Immediate Functions
Parameter Pack and Fold Expressions
Constexpr If Statements

## Slide 5
source code
Methodology
cross-compilation
arm-none-eabi 10.3.1
STM32F030CC
objdump
st-flash
compilation time
runtime performance (analytical)
runtime performance (empirical)
binary size
binary
analysis of disassembled binary
measurement of runtime performance

## Slide 6
Base Firmware
Absolute minimal embedded project:
  Startup script:
      Defines the vector table
      Sets stack pointer
      Copies data section from flash to RAM
      Initializes uninitialized global and static variables to zero
      Calls static constructors
      Calls main()
  Linker Script: specifies the memory layout
  Main function:
      Entry point of the firmware
      Consists of a single, empty infinite loop
2092 bytes
  text: 524 bytes
  data: 0 bytes
  bss: 1568 bytes

## Slide 7
Inefficiencies in HAL
Enums are basically integers with no value restrictions
Runtime branching based on input parameters
Runtime bitmask calculations
C++ support = extern “C”
typedef struct {
uint32_t pin;
GPIO_Modes mode;
} GPIO_InitStruct;
void GPIO_Init(GPIO_InitStruct* conf) {
uint32_t temp;
/* check the values */
if (!IS_GPIO_PIN(conf->pin)) { return; }
if (!IS_GPIO_MODE(conf->mode)) { return; }
/* configure the GPIO based on the settings */
if (conf->mode == GPIO_MODE_OUTPUT) {
temp = OSPEEDR;
temp &= ~(OSPEEDR_MASK << (conf->pin * 2u));
temp |= (GPIO_SPEED_FREQ_LOW << (conf->pin * 2u));
OSPEEDR = temp;
/* ... */
}
/* ... */
}

## Slide 8
Inefficiencies in HAL
int main (void) {
GPIO_InitStruct conf = { 0 };
conf.pin = GPIO_PIN_6;
conf.mode = GPIO_MODE_INPUT;
GPIO_Init(&conf) ;
while (1) { }
}
<main>:
movs r3, #6
push {r0, r1, r2, lr}
str r3, [sp, #0]
mov r0, sp
subs r3, #5
str r3, [sp, #4]
bl 8000198 <GPIO_Init>
b.n 80001f4 <main+0x10>
set up the pin value for GPIO_PIN_6 (value 6)

## Slide 9
Inefficiencies in HAL
int main (void) {
GPIO_InitStruct conf = { 0 };
conf.pin = GPIO_PIN_6;
conf.mode = GPIO_MODE_INPUT;
GPIO_Init(&conf) ;
while (1) { }
}
<main>:
movs r3, #6
push {r0, r1, r2, lr}
str r3, [sp, #0]
mov r0, sp
subs r3, #5
str r3, [sp, #4]
bl 8000198 <GPIO_Init>
b.n 80001f4 <main+0x10>
prepare for calling a function by saving the current state

## Slide 10
Inefficiencies in HAL
int main (void) {
GPIO_InitStruct conf = { 0 };
conf.pin = GPIO_PIN_6;
conf.mode = GPIO_MODE_INPUT;
GPIO_Init(&conf) ;
while (1) { }
}
<main>:
movs r3, #6
push {r0, r1, r2, lr}
str r3, [sp, #0]
mov r0, sp
subs r3, #5
str r3, [sp, #4]
bl 8000198 <GPIO_Init>
b.n 80001f4 <main+0x10>
store the pin value in the GPIO_InitStruct structure on the stack

## Slide 11
Inefficiencies in HAL
int main (void) {
GPIO_InitStruct conf = { 0 };
conf.pin = GPIO_PIN_6;
conf.mode = GPIO_MODE_INPUT;
GPIO_Init(&conf) ;
while (1) { }
}
<main>:
movs r3, #6
push {r0, r1, r2, lr}
str r3, [sp, #0]
mov r0, sp
subs r3, #5
str r3, [sp, #4]
bl 8000198 <GPIO_Init>
b.n 80001f4 <main+0x10>
prepare to pass the address of the GPIO_InitStruct
structure to the GPIO_Init function

## Slide 12
Inefficiencies in HAL
int main (void) {
GPIO_InitStruct conf = { 0 };
conf.pin = GPIO_PIN_6;
conf.mode = GPIO_MODE_INPUT;
GPIO_Init(&conf) ;
while (1) { }
}
<main>:
movs r3, #6
push {r0, r1, r2, lr}
str r3, [sp, #0]
mov r0, sp
subs r3, #5
str r3, [sp, #4]
bl 8000198 <GPIO_Init>
b.n 80001f4 <main+0x10>
set up the mode value for GPIO_MODE_INPUT (subtract 5 from 6 -> 1)

## Slide 13
Inefficiencies in HAL
int main (void) {
GPIO_InitStruct conf = { 0 };
conf.pin = GPIO_PIN_6;
conf.mode = GPIO_MODE_INPUT;
GPIO_Init(&conf) ;
while (1) { }
}
<main>:
movs r3, #6
push {r0, r1, r2, lr}
str r3, [sp, #0]
mov r0, sp
subs r3, #5
str r3, [sp, #4]
bl 8000198 <GPIO_Init>
b.n 80001f4 <main+0x10>
store the mode value in the GPIO_InitStruct structure on the stack

## Slide 14
Inefficiencies in HAL
int main (void) {
GPIO_InitStruct conf = { 0 };
conf.pin = GPIO_PIN_6;
conf.mode = GPIO_MODE_INPUT;
GPIO_Init(&conf) ;
while (1) { }
}
<main>:
movs r3, #6
push {r0, r1, r2, lr}
str r3, [sp, #0]
mov r0, sp
subs r3, #5
str r3, [sp, #4]
bl 8000198 <GPIO_Init>
b.n 80001f4 <main+0x10>
call the GPIO_Init function with the GPIO_InitStruct
structure as an argument

## Slide 15
Inefficiencies in HAL
int main (void) {
GPIO_InitStruct conf = { 0 };
conf.pin = GPIO_PIN_6;
conf.mode = GPIO_MODE_INPUT;
GPIO_Init(&conf) ;
while (1) { }
}
<main>:
movs r3, #6
push {r0, r1, r2, lr}
str r3, [sp, #0]
mov r0, sp
subs r3, #5
str r3, [sp, #4]
bl 8000198 <GPIO_Init>
b.n 80001f4 <main+0x10>
create an infinite loop (branch to the same address)

## Slide 16
Inefficiencies in HAL
typedef struct {
uint32_t pin;
GPIO_Modes mode;
} GPIO_InitStruct;
void GPIO_Init(GPIO_InitStruct* conf) {
uint32_t temp;
/* check the values */
if (!IS_GPIO_PIN(conf->pin)) { return; }
if (!IS_GPIO_MODE(conf->mode)) { return; }
/* configure the GPIO based on the settings */
if (conf->mode == GPIO_MODE_OUTPUT) {
temp = OSPEEDR;
temp &= ~(OSPEEDR_MASK << (conf->pin * 2u));
temp |= (GPIO_SPEED_FREQ_LOW << (conf->pin * 2u));
OSPEEDR = temp;
/* ... */
}
/* ... */
}
ldr r2, [r0, #0]
push {r4, r5, lr}
cmp r2, #15
bhi.n 80001da <GPIO_Init+0x42>
ldrb r3, [r0, #4]
cmp r3, #1
bhi.n 80001da <GPIO_Init+0x42>
bne.n 80001c4 <GPIO_Init+0x2c>
movs r4, #3
lsls r2, r2, #1
lsls r4, r2
ldr r5, [pc, #44]
ldr r1, [r5, #0]
bics r1, r4
movs r4, r3
str r1, [r5, #0]
if pin is greater than 15, branch to the end (invalid pin check)

## Slide 17
Inefficiencies in HAL
typedef struct {
uint32_t pin;
GPIO_Modes mode;
} GPIO_InitStruct;
void GPIO_Init(GPIO_InitStruct* conf) {
uint32_t temp;
/* check the values */
if (!IS_GPIO_PIN(conf->pin)) { return; }
if (!IS_GPIO_MODE(conf->mode)) { return; }
/* configure the GPIO based on the settings */
if (conf->mode == GPIO_MODE_OUTPUT) {
temp = OSPEEDR;
temp &= ~(OSPEEDR_MASK << (conf->pin * 2u));
temp |= (GPIO_SPEED_FREQ_LOW << (conf->pin * 2u));
OSPEEDR = temp;
/* ... */
}
/* ... */
}
ldr r2, [r0, #0]
push {r4, r5, lr}
cmp r2, #15
bhi.n 80001da <GPIO_Init+0x42>
ldrb r3, [r0, #4]
cmp r3, #1
bhi.n 80001da <GPIO_Init+0x42>
bne.n 80001c4 <GPIO_Init+0x2c>
movs r4, #3
lsls r2, r2, #1
lsls r4, r2
ldr r5, [pc, #44]
ldr r1, [r5, #0]
bics r1, r4
movs r4, r3
str r1, [r5, #0]
if mode is greater than 1, branch to the end (invalid mode check)

## Slide 18
Inefficiencies in HAL
typedef struct {
uint32_t pin;
GPIO_Modes mode;
} GPIO_InitStruct;
void GPIO_Init(GPIO_InitStruct* conf) {
uint32_t temp;
/* check the values */
if (!IS_GPIO_PIN(conf->pin)) { return; }
if (!IS_GPIO_MODE(conf->mode)) { return; }
/* configure the GPIO based on the settings */
if (conf->mode == GPIO_MODE_OUTPUT) {
temp = OSPEEDR;
temp &= ~(OSPEEDR_MASK << (conf->pin * 2u));
temp |= (GPIO_SPEED_FREQ_LOW << (conf->pin * 2u));
OSPEEDR = temp;
/* ... */
}
/* ... */
}
ldr r2, [r0, #0]
push {r4, r5, lr}
cmp r2, #15
bhi.n 80001da <GPIO_Init+0x42>
ldrb r3, [r0, #4]
cmp r3, #1
bhi.n 80001da <GPIO_Init+0x42>
bne.n 80001c4 <GPIO_Init+0x2c>
movs r4, #3
lsls r2, r2, #1
lsls r4, r2
ldr r5, [pc, #44]
ldr r1, [r5, #0]
bics r1, r4
movs r4, r3
str r1, [r5, #0]
if mode is not 1, branch to configure pin for input mode

## Slide 19
Inefficiencies in HAL
typedef struct {
uint32_t pin;
GPIO_Modes mode;
} GPIO_InitStruct;
void GPIO_Init(GPIO_InitStruct* conf) {
uint32_t temp;
/* check the values */
if (!IS_GPIO_PIN(conf->pin)) { return; }
if (!IS_GPIO_MODE(conf->mode)) { return; }
/* configure the GPIO based on the settings */
if (conf->mode == GPIO_MODE_OUTPUT) {
temp = OSPEEDR;
temp &= ~(OSPEEDR_MASK << (conf->pin * 2u));
temp |= (GPIO_SPEED_FREQ_LOW << (conf->pin * 2u));
OSPEEDR = temp;
/* ... */
}
/* ... */
}
ldr r2, [r0, #0]
push {r4, r5, lr}
cmp r2, #15
bhi.n 80001da <GPIO_Init+0x42>
ldrb r3, [r0, #4]
cmp r3, #1
bhi.n 80001da <GPIO_Init+0x42>
bne.n 80001c4 <GPIO_Init+0x2c>
movs r4, #3
lsls r2, r2, #1
lsls r4, r2
ldr r5, [pc, #44]
ldr r1, [r5, #0]
bics r1, r4
movs r4, r3
str r1, [r5, #0]
prepare mask value for OSPEEDR (3)

## Slide 20
Inefficiencies in HAL
typedef struct {
uint32_t pin;
GPIO_Modes mode;
} GPIO_InitStruct;
void GPIO_Init(GPIO_InitStruct* conf) {
uint32_t temp;
/* check the values */
if (!IS_GPIO_PIN(conf->pin)) { return; }
if (!IS_GPIO_MODE(conf->mode)) { return; }
/* configure the GPIO based on the settings */
if (conf->mode == GPIO_MODE_OUTPUT) {
temp = OSPEEDR;
temp &= ~(OSPEEDR_MASK << (conf->pin * 2u));
temp |= (GPIO_SPEED_FREQ_LOW << (conf->pin * 2u));
OSPEEDR = temp;
/* ... */
}
/* ... */
}
ldr r2, [r0, #0]
push {r4, r5, lr}
cmp r2, #15
bhi.n 80001da <GPIO_Init+0x42>
ldrb r3, [r0, #4]
cmp r3, #1
bhi.n 80001da <GPIO_Init+0x42>
bne.n 80001c4 <GPIO_Init+0x2c>
movs r4, #3
lsls r2, r2, #1
lsls r4, r2
ldr r5, [pc, #44]
ldr r1, [r5, #0]
bics r1, r4
movs r4, r3
str r1, [r5, #0]
shift pin value left by 1 bit (pin * 2)

## Slide 21
Inefficiencies in HAL
typedef struct {
uint32_t pin;
GPIO_Modes mode;
} GPIO_InitStruct;
void GPIO_Init(GPIO_InitStruct* conf) {
uint32_t temp;
/* check the values */
if (!IS_GPIO_PIN(conf->pin)) { return; }
if (!IS_GPIO_MODE(conf->mode)) { return; }
/* configure the GPIO based on the settings */
if (conf->mode == GPIO_MODE_OUTPUT) {
temp = OSPEEDR;
temp &= ~(OSPEEDR_MASK << (conf->pin * 2u));
temp |= (GPIO_SPEED_FREQ_LOW << (conf->pin * 2u));
OSPEEDR = temp;
/* ... */
}
/* ... */
}
ldr r2, [r0, #0]
push {r4, r5, lr}
cmp r2, #15
bhi.n 80001da <GPIO_Init+0x42>
ldrb r3, [r0, #4]
cmp r3, #1
bhi.n 80001da <GPIO_Init+0x42>
bne.n 80001c4 <GPIO_Init+0x2c>
movs r4, #3
lsls r2, r2, #1
lsls r4, r2
ldr r5, [pc, #44]
ldr r1, [r5, #0]
bics r1, r4
movs r4, r3
str r1, [r5, #0]
shift mask value left by (pin * 2) positions

## Slide 22
Inefficiencies in HAL
typedef struct {
uint32_t pin;
GPIO_Modes mode;
} GPIO_InitStruct;
void GPIO_Init(GPIO_InitStruct* conf) {
uint32_t temp;
/* check the values */
if (!IS_GPIO_PIN(conf->pin)) { return; }
if (!IS_GPIO_MODE(conf->mode)) { return; }
/* configure the GPIO based on the settings */
if (conf->mode == GPIO_MODE_OUTPUT) {
temp = OSPEEDR;
temp &= ~(OSPEEDR_MASK << (conf->pin * 2u));
temp |= (GPIO_SPEED_FREQ_LOW << (conf->pin * 2u));
OSPEEDR = temp;
/* ... */
}
/* ... */
}
ldr r2, [r0, #0]
push {r4, r5, lr}
cmp r2, #15
bhi.n 80001da <GPIO_Init+0x42>
ldrb r3, [r0, #4]
cmp r3, #1
bhi.n 80001da <GPIO_Init+0x42>
bne.n 80001c4 <GPIO_Init+0x2c>
movs r4, #3
lsls r2, r2, #1
lsls r4, r2
ldr r5, [pc, #44]
ldr r1, [r5, #0]
bics r1, r4
movs r4, r3
str r1, [r5, #0]
load address of OSPEEDR into r5

## Slide 23
Inefficiencies in HAL
typedef struct {
uint32_t pin;
GPIO_Modes mode;
} GPIO_InitStruct;
void GPIO_Init(GPIO_InitStruct* conf) {
uint32_t temp;
/* check the values */
if (!IS_GPIO_PIN(conf->pin)) { return; }
if (!IS_GPIO_MODE(conf->mode)) { return; }
/* configure the GPIO based on the settings */
if (conf->mode == GPIO_MODE_OUTPUT) {
temp = OSPEEDR;
temp &= ~(OSPEEDR_MASK << (conf->pin * 2u));
temp |= (GPIO_SPEED_FREQ_LOW << (conf->pin * 2u));
OSPEEDR = temp;
/* ... */
}
/* ... */
}
ldr r2, [r0, #0]
push {r4, r5, lr}
cmp r2, #15
bhi.n 80001da <GPIO_Init+0x42>
ldrb r3, [r0, #4]
cmp r3, #1
bhi.n 80001da <GPIO_Init+0x42>
bne.n 80001c4 <GPIO_Init+0x2c>
movs r4, #3
lsls r2, r2, #1
lsls r4, r2
ldr r5, [pc, #44]
ldr r1, [r5, #0]
bics r1, r4
movs r4, r3
str r1, [r5, #0]
load current OSPEEDR value into r1

## Slide 24
Inefficiencies in HAL
typedef struct {
uint32_t pin;
GPIO_Modes mode;
} GPIO_InitStruct;
void GPIO_Init(GPIO_InitStruct* conf) {
uint32_t temp;
/* check the values */
if (!IS_GPIO_PIN(conf->pin)) { return; }
if (!IS_GPIO_MODE(conf->mode)) { return; }
/* configure the GPIO based on the settings */
if (conf->mode == GPIO_MODE_OUTPUT) {
temp = OSPEEDR;
temp &= ~(OSPEEDR_MASK << (conf->pin * 2u));
temp |= (GPIO_SPEED_FREQ_LOW << (conf->pin * 2u));
OSPEEDR = temp;
/* ... */
}
/* ... */
}
ldr r2, [r0, #0]
push {r4, r5, lr}
cmp r2, #15
bhi.n 80001da <GPIO_Init+0x42>
ldrb r3, [r0, #4]
cmp r3, #1
bhi.n 80001da <GPIO_Init+0x42>
bne.n 80001c4 <GPIO_Init+0x2c>
movs r4, #3
lsls r2, r2, #1
lsls r4, r2
ldr r5, [pc, #44]
ldr r1, [r5, #0]
bics r1, r4
movs r4, r3
str r1, [r5, #0]
clear the two bits for the pin in OSPEEDR

## Slide 25
Inefficiencies in HAL
typedef struct {
uint32_t pin;
GPIO_Modes mode;
} GPIO_InitStruct;
void GPIO_Init(GPIO_InitStruct* conf) {
uint32_t temp;
/* check the values */
if (!IS_GPIO_PIN(conf->pin)) { return; }
if (!IS_GPIO_MODE(conf->mode)) { return; }
/* configure the GPIO based on the settings */
if (conf->mode == GPIO_MODE_OUTPUT) {
temp = OSPEEDR;
temp &= ~(OSPEEDR_MASK << (conf->pin * 2u));
temp |= (GPIO_SPEED_FREQ_LOW << (conf->pin * 2u));
OSPEEDR = temp;
/* ... */
}
/* ... */
}
ldr r2, [r0, #0]
push {r4, r5, lr}
cmp r2, #15
bhi.n 80001da <GPIO_Init+0x42>
ldrb r3, [r0, #4]
cmp r3, #1
bhi.n 80001da <GPIO_Init+0x42>
bne.n 80001c4 <GPIO_Init+0x2c>
movs r4, #3
lsls r2, r2, #1
lsls r4, r2
ldr r5, [pc, #44]
ldr r1, [r5, #0]
bics r1, r4
movs r4, r3
str r1, [r5, #0]
GPIO_SPEED_FREQ_LOW is 0 -> optimized

## Slide 26
Inefficiencies in HAL
typedef struct {
uint32_t pin;
GPIO_Modes mode;
} GPIO_InitStruct;
void GPIO_Init(GPIO_InitStruct* conf) {
uint32_t temp;
/* check the values */
if (!IS_GPIO_PIN(conf->pin)) { return; }
if (!IS_GPIO_MODE(conf->mode)) { return; }
/* configure the GPIO based on the settings */
if (conf->mode == GPIO_MODE_OUTPUT) {
temp = OSPEEDR;
temp &= ~(OSPEEDR_MASK << (conf->pin * 2u));
temp |= (GPIO_SPEED_FREQ_LOW << (conf->pin * 2u));
OSPEEDR = temp;
/* ... */
}
/* ... */
}
ldr r2, [r0, #0]
push {r4, r5, lr}
cmp r2, #15
bhi.n 80001da <GPIO_Init+0x42>
ldrb r3, [r0, #4]
cmp r3, #1
bhi.n 80001da <GPIO_Init+0x42>
bne.n 80001c4 <GPIO_Init+0x2c>
movs r4, #3
lsls r2, r2, #1
lsls r4, r2
ldr r5, [pc, #44]
ldr r1, [r5, #0]
bics r1, r4
movs r4, r3
str r1, [r5, #0]
store the modified OSPEEDR value back

## Slide 27
Building Layers of Abstractions
Take the original C code, modify as little as possible, focusing only on the abstraction in question.
Compare the binary size, compilation time (generated code) and the runtime performance (analytically now, empirically probably only at the end).
C code

## Slide 28
Building Layers of Abstractions
Take the original C code, modify as little as possible, focusing only on the abstraction in question.
Compare the binary size, compilation time (generated code) and the runtime performance (analytically now, empirically probably only at the end).
C code
C++ code

## Slide 29
Encapsulation

## Slide 30
Encapsulation

## Slide 31
Encapsulation
(basic)
class CRegister {
private:
const std::uint32_t m_address;
public:
CRegister (std::uint32_t address) : m_address(address) { }
void set (std::uint32_t val) const {
*(reinterpret_cast<volatile std::uint32_t *>(m_address)) = val;
}
/* ... */
};

## Slide 32
Encapsulation
(basic)
class CRegister {
private:
const std::uint32_t m_address;
public:
CRegister (std::uint32_t address) : m_address(address) { }
void set (std::uint32_t val) const {
*(reinterpret_cast<volatile std::uint32_t *>(m_address)) = val;
}
/* ... */
};

## Slide 33
Encapsulation
(basic)
class CRegister {
private:
const std::uint32_t m_address;
public:
CRegister (std::uint32_t address) : m_address(address) { }
void set (std::uint32_t val) const {
*(reinterpret_cast<volatile std::uint32_t *>(m_address)) = val;
}
/* ... */
};

## Slide 34
Encapsulation
(basic)
class CRegister {
private:
const std::uint32_t m_address;
public:
CRegister (std::uint32_t address) : m_address(address) { }
void set (std::uint32_t val) const {
*(reinterpret_cast<volatile std::uint32_t *>(m_address)) = val;
}
/* ... */
};

## Slide 35
Encapsulation
(basic)
class CRegister {
private:
const std::uint32_t m_address;
public:
CRegister (std::uint32_t address) : m_address(address) { }
void set (std::uint32_t val) const {
*(reinterpret_cast<volatile std::uint32_t *>(m_address)) = val;
}
/* ... */
};
temp = OSPEEDR;
temp &= ~(OSPEEDR_MASK << (conf->pin * 2u));
temp |= (conf->speed << (conf->pin * 2u));
OSPEEDR = temp;

## Slide 36
Encapsulation

## Slide 37
Encapsulation
(basic)
class CModeRegister {
private:
const CRegister m_register { 0x48000000 };
inline std::uint32_t calculate_value (std::uint32_t pin, GPIO_Modes mode) {
return (mode & GPIO_MODE) << (pin * 2);
}
inline std::uint32_t calculate_bitmask (std::uint32_t pin) {
return MODER_MASK << (pin * 2);
}
public:
inline void set_mode (std::uint32_t pin, GPIO_Modes mode) {
m_register.set(calculate_value(pin, mode), calculate_bitmask(pin));
}
};

## Slide 38
Encapsulation
(basic)
class CModeRegister {
private:
const CRegister m_register { 0x48000000 };
inline std::uint32_t calculate_value (std::uint32_t pin, GPIO_Modes mode) {
return (mode & GPIO_MODE) << (pin * 2);
}
inline std::uint32_t calculate_bitmask (std::uint32_t pin) {
return MODER_MASK << (pin * 2);
}
public:
inline void set_mode (std::uint32_t pin, GPIO_Modes mode) {
m_register.set(calculate_value(pin, mode), calculate_bitmask(pin));
}
};

## Slide 39
Encapsulation
(basic)
class CModeRegister {
private:
const CRegister m_register { 0x48000000 };
inline std::uint32_t calculate_value (std::uint32_t pin, GPIO_Modes mode) {
return (mode & GPIO_MODE) << (pin * 2);
}
inline std::uint32_t calculate_bitmask (std::uint32_t pin) {
return MODER_MASK << (pin * 2);
}
public:
inline void set_mode (std::uint32_t pin, GPIO_Modes mode) {
m_register.set(calculate_value(pin, mode), calculate_bitmask(pin));
}
};

## Slide 40
Encapsulation
(basic)
class CModeRegister {
private:
const CRegister m_register { 0x48000000 };
inline std::uint32_t calculate_value (std::uint32_t pin, GPIO_Modes mode) {
return (mode & GPIO_MODE) << (pin * 2);
}
inline std::uint32_t calculate_bitmask (std::uint32_t pin) {
return MODER_MASK << (pin * 2);
}
public:
inline void set_mode (std::uint32_t pin, GPIO_Modes mode) {
m_register.set(calculate_value(pin, mode), calculate_bitmask(pin));
}
};

## Slide 41
Encapsulation
(basic)
class CModeRegister {
private:
const CRegister m_register { 0x48000000 };
inline std::uint32_t calculate_value (std::uint32_t pin, GPIO_Modes mode) {
return (mode & GPIO_MODE) << (pin * 2);
}
inline std::uint32_t calculate_bitmask (std::uint32_t pin) {
return MODER_MASK << (pin * 2);
}
public:
inline void set_mode (std::uint32_t pin, GPIO_Modes mode) {
m_register.set(calculate_value(pin, mode), calculate_bitmask(pin));
}
};
temp = OSPEEDR;
temp &= ~(OSPEEDR_MASK << (conf->pin * 2u));
temp |= (conf->speed << (conf->pin * 2u));
OSPEEDR = temp;

## Slide 42
Encapsulation
(basic)
void GPIO_Init(GPIO_InitStruct* conf) {
/* ... */
if (conf->mode == GPIO_MODE_OUTPUT) {
COutputSpeedRegister ospeedr {};
ospeedr.set_speed(conf->pin, conf->speed);
COutputTypeRegister otyper {};
otyper.set_type(conf->pin, conf->type);
}
CModeRegister moder {};
moder.set_mode(conf->pin, conf->mode);
/* ... */
}
void GPIO_Init(GPIO_InitStruct* conf) {
/* ... */
if (conf->mode == GPIO_MODE_OUTPUT) {
temp = OSPEEDR;
temp &= ~(OSPEEDR_MASK << (conf->pin * 2u));
temp |= (conf->speed << (conf->pin * 2u));
OSPEEDR = temp;
temp = OTYPER;
temp &= ~(OTYPER_MASK << conf->pin);
temp |= (((conf->type & GPIO_OUTPUT_TYPE) >> 4u)
<< conf->pin);
OTYPER = temp;
}
temp = MODER;
temp &= ~(MODER_MASK << (conf->pin * 2u));
temp |= ((conf->mode & GPIO_MODE) << (conf->pin * 2u));
MODER = temp;
/* ... */
}

## Slide 43
Encapsulation
(basic)
Compiles to the same binary.
TODO : compilation time?

## Slide 44
Encapsulation
(static)
void GPIO_Init(GPIO_InitStruct* conf) {
/* check the values */
if (!IS_GPIO_PIN(conf->pin)) { return; }
if (!IS_GPIO_MODE(conf->mode)) { return; }
/* configure the GPIO based on the settings */
if (conf->mode == GPIO_MODE_OUTPUT) {
COutputSpeedRegister::set_speed(conf->pin, conf->speed);
COutputTypeRegister::set_type(conf->pin, conf->type);
}
CModeRegister::set_mode(conf->pin, conf->mode);
/* ... */
}

## Slide 45
Encapsulation
(static)
class CModeRegister {
private:
static inline const CRegister m_register { 0x48000000 };
static inline std::uint32_t calculate_value (std::uint32_t pin, GPIO_Modes mode) {
return (mode & GPIO_MODE) << (pin * 2);
}
static inline std::uint32_t calculate_bitmask (std::uint32_t pin) {
return MODER_MASK << (pin * 2);
}
public:
static inline void set_mode (std::uint32_t pin, GPIO_Modes mode) {
m_register.set(calculate_value(pin, mode), calculate_bitmask(pin));
}
};

## Slide 46
Encapsulation
(static)
Binary size increase… why?

## Slide 47
Encapsulation
(static)
_GLOBAL__sub_I__Z9GPIO_InitP15GPIO_InitStruct
Objects with static storage duration need to be initialized before the main function starts executing.
This function initializes the static CRegister objects and loads the values used in the static member functions of the register classes.
Does not affect runtime performance, as it executes before the main function, but it increases binary size.

## Slide 48
template <std::uint32_t address>
class CRegister {
public:
void set (std::uint32_t val) const {
*(reinterpret_cast<volatile std::uint32_t *>(address)) = val;
}
/* ... */
};
Encapsulation
(static & template)

## Slide 49
class CModeRegister {
private:
static inline const CRegister<0x48000000> m_register { };
/* ... */
};
Encapsulation
(static & template)
class CModeRegister {
private:
static inline const CRegister m_register { 0x48000000 };
/* ... */
};

## Slide 50
Encapsulation
(static & template)
Binary size is back to the original.
Each CRegister instance is fully defined at compile time.
No global state that needs to be explicitly initialized before main.
Compiler can better optimize the code at compile time.

## Slide 51
Inheritance
class COutputSpeedRegister : public CRegister<0x48000008> {
private:
static inline std::uint32_t calculate_value (std::uint32_t pin, GPIO_Output_Speeds speed) {
return speed << (pin * 2);
}
static inline std::uint32_t calculate_bitmask (std::uint32_t pin) {
return OSPEEDR_MASK << (pin * 2);
}
public:
static inline void set_speed (std::uint32_t pin, GPIO_Output_Speeds speed) {
set(calculate_value(pin, speed), calculate_bitmask(pin));
}
};

## Slide 52
Inheritance
Compiles to the same binary.

## Slide 53
Dynamic Polymorphism

## Slide 54
Static Polymorphism

## Slide 55
Runtime bitmask calculations
Runtime branching
Function calls
Runtime input validation
Inefficiencies in HAL

## Slide 56
Runtime bitmask calculations
Runtime branching
Function calls
Runtime input validation
Inefficiencies in HAL

## Slide 57
This is about the “special” cases where the hardware is known, which is common for embedded systems.
I did not replace the HAL given by the manufacturer, I extended it.
The same techniques can be used in any other application as well, if the circumstances allow it.
These are no guidelines or rules.
Notes

## Slide 58
Enumerations
enum class modes : std::uint32_t {
input = 0b00,
output = 0b01,
alt_func = 0b10,
analog = 0b11
};
enum class ports : std::uint8_t {
port_f,
port_d,
port_c,
port_b,
port_a
};
Enumerations
  Not plain integers anymore
  No implicit conversions between enum values and integral types
      Explicit static_cast required
      Harder to misuse accidentally

## Slide 59
Concepts
template <modes mode>
concept is_valid_mode = (
(mode == modes::input) ||
(mode == modes::output) ||
(mode == modes::alt_func) ||
(mode == modes::analog)
);
template <pins pin>
concept is_valid_pin = (
is_valid_low_pin<pin> || is_valid_high_pin<pin>
);
template <pins... pin>
concept are_valid_pins = (is_valid_pin<pin> && ...);

## Slide 60
Immediate Functions
template <modes mode, pins... pin>
requires (are_valid_pins<pin ...> && is_valid_mode<mode>)
consteval std::uint32_t moder_value () {
return (... | (static_cast<std::uint32_t>(mode) <<
(static_cast<std::uint32_t>(pin) * 2)));
}
template <pins... pin>
requires (are_valid_pins<pin ...>)
consteval std::uint32_t moder_bitmask () {
return (... | (GPIO_MODER_MODER0 <<
(static_cast<std::uint32_t>(pin) * 2)));
}

## Slide 61
Compile-time Branching

## Slide 62
Measurement