## Slide 1: Balancing Efficiency and Flexibility
Cost of Abstractions in Embedded Systems Marcell Juhasz
Notes: Hello Everyone! I am Marcell Juhasz. Welcome to my presentation about the cost of abstractions in embedded systems.

## Slide 2
whoami
Marcell Juhasz
github.com/juhaszmarcell96
linkedin.com/in/juhaszmarcell
marcell.juhasz96@gmail.com
Zühlke Engineering (Austria) GmbH
Rivergate, Handelskai 92
1200, Vienna, Austria
wien@zuehlke.com
+43 1 205 11 6800

## Slide 3
Motivation
C is dominant in the embedded world
  direct interaction with hardware
  flexible
  robust
  efficient
Common opinions:
  C is as efficient as it gets
  abstraction = less efficient software
  C++ comes with inherent runtime overhead

## Slide 4
Overview
Hardware Abstraction Layer
Encapsulation
Inheritance
Polymorphism
+
Template Metaprogramming
Concepts
Constant Expressions
Immediate Functions
Parameter Pack and Fold Expressions
Constexpr If Statements

## Slide 5
source code
Methodology
cross-compilation
arm-none-eabi 10.3.1
STM32F030CC
-Os
objdump
st-flash
compilation time
runtime performance (analytical)
runtime performance (empirical)
binary size
binary
analysis of disassembled binary
measurement of runtime performance

## Slide 6
Base Firmware
Absolute minimal embedded project:
  Startup script:
      Defines the vector table
      Sets stack pointer
      Copies data section from flash to RAM
      Initializes uninitialized global and static variables to zero
      Calls static constructors
      Calls main()
  Linker Script: specifies the memory layout
  Main function:
      Entry point of the firmware
      Consists of a single, empty infinite loop
2092 bytes
  text: 524 bytes
  data: 0 bytes
  bss: 1568 bytes

## Slide 7
Inefficiencies in HAL
Enums are basically integers with no value restrictions
Runtime branching based on input parameters
Runtime bitmask calculations
C++ support = extern “C”
typedef struct {
uint32_t pin;
GPIO_Modes mode;
} GPIO_InitStruct;
void GPIO_Init(GPIO_InitStruct* conf) {
uint32_t temp;
/* check the values */
if (!IS_GPIO_PIN(conf->pin)) { return; }
if (!IS_GPIO_MODE(conf->mode)) { return; }
/* configure the GPIO based on the settings */
if (conf->mode == GPIO_MODE_OUTPUT) {
temp = OSPEEDR;
temp &= ~(OSPEEDR_MASK << (conf->pin * 2u));
temp |= (GPIO_SPEED_FREQ_LOW << (conf->pin * 2u));
OSPEEDR = temp;
/* ... */
}
/* ... */
}

## Slide 8
Inefficiencies in HAL
int main (void) {
GPIO_InitStruct conf = { 0 };
conf.pin = GPIO_PIN_6;
conf.mode = GPIO_MODE_INPUT;
GPIO_Init(&conf) ;
while (1) { }
}
<main>:
movs r3, #6
push {r0, r1, r2, lr}
str r3, [sp, #0]
mov r0, sp
subs r3, #5
str r3, [sp, #4]
bl 8000198 <GPIO_Init>
b.n 80001f4 <main+0x10>
set up the pin value for GPIO_PIN_6 (value 6)

## Slide 9
Inefficiencies in HAL
int main (void) {
GPIO_InitStruct conf = { 0 };
conf.pin = GPIO_PIN_6;
conf.mode = GPIO_MODE_INPUT;
GPIO_Init(&conf) ;
while (1) { }
}
<main>:
movs r3, #6
push {r0, r1, r2, lr}
str r3, [sp, #0]
mov r0, sp
subs r3, #5
str r3, [sp, #4]
bl 8000198 <GPIO_Init>
b.n 80001f4 <main+0x10>
prepare for calling a function by saving the current state

## Slide 10
Inefficiencies in HAL
int main (void) {
GPIO_InitStruct conf = { 0 };
conf.pin = GPIO_PIN_6;
conf.mode = GPIO_MODE_INPUT;
GPIO_Init(&conf) ;
while (1) { }
}
<main>:
movs r3, #6
push {r0, r1, r2, lr}
str r3, [sp, #0]
mov r0, sp
subs r3, #5
str r3, [sp, #4]
bl 8000198 <GPIO_Init>
b.n 80001f4 <main+0x10>
store the pin value in the GPIO_InitStruct structure on the stack

## Slide 11
Inefficiencies in HAL
int main (void) {
GPIO_InitStruct conf = { 0 };
conf.pin = GPIO_PIN_6;
conf.mode = GPIO_MODE_INPUT;
GPIO_Init(&conf) ;
while (1) { }
}
<main>:
movs r3, #6
push {r0, r1, r2, lr}
str r3, [sp, #0]
mov r0, sp
subs r3, #5
str r3, [sp, #4]
bl 8000198 <GPIO_Init>
b.n 80001f4 <main+0x10>
prepare to pass the address of the GPIO_InitStruct
structure to the GPIO_Init function

## Slide 12
Inefficiencies in HAL
int main (void) {
GPIO_InitStruct conf = { 0 };
conf.pin = GPIO_PIN_6;
conf.mode = GPIO_MODE_INPUT;
GPIO_Init(&conf) ;
while (1) { }
}
<main>:
movs r3, #6
push {r0, r1, r2, lr}
str r3, [sp, #0]
mov r0, sp
subs r3, #5
str r3, [sp, #4]
bl 8000198 <GPIO_Init>
b.n 80001f4 <main+0x10>
set up the mode value for GPIO_MODE_INPUT (subtract 5 from 6 -> 1)

## Slide 13
Inefficiencies in HAL
int main (void) {
GPIO_InitStruct conf = { 0 };
conf.pin = GPIO_PIN_6;
conf.mode = GPIO_MODE_INPUT;
GPIO_Init(&conf) ;
while (1) { }
}
<main>:
movs r3, #6
push {r0, r1, r2, lr}
str r3, [sp, #0]
mov r0, sp
subs r3, #5
str r3, [sp, #4]
bl 8000198 <GPIO_Init>
b.n 80001f4 <main+0x10>
store the mode value in the GPIO_InitStruct structure on the stack

## Slide 14
Inefficiencies in HAL
int main (void) {
GPIO_InitStruct conf = { 0 };
conf.pin = GPIO_PIN_6;
conf.mode = GPIO_MODE_INPUT;
GPIO_Init(&conf) ;
while (1) { }
}
<main>:
movs r3, #6
push {r0, r1, r2, lr}
str r3, [sp, #0]
mov r0, sp
subs r3, #5
str r3, [sp, #4]
bl 8000198 <GPIO_Init>
b.n 80001f4 <main+0x10>
call the GPIO_Init function with the GPIO_InitStruct
structure as an argument

## Slide 15
Inefficiencies in HAL
int main (void) {
GPIO_InitStruct conf = { 0 };
conf.pin = GPIO_PIN_6;
conf.mode = GPIO_MODE_INPUT;
GPIO_Init(&conf) ;
while (1) { }
}
<main>:
movs r3, #6
push {r0, r1, r2, lr}
str r3, [sp, #0]
mov r0, sp
subs r3, #5
str r3, [sp, #4]
bl 8000198 <GPIO_Init>
b.n 80001f4 <main+0x10>
create an infinite loop (branch to the same address)

## Slide 16
Inefficiencies in HAL
typedef struct {
uint32_t pin;
GPIO_Modes mode;
} GPIO_InitStruct;
void GPIO_Init(GPIO_InitStruct* conf) {
uint32_t temp;
/* check the values */
if (!IS_GPIO_PIN(conf->pin)) { return; }
if (!IS_GPIO_MODE(conf->mode)) { return; }
/* configure the GPIO based on the settings */
if (conf->mode == GPIO_MODE_OUTPUT) {
temp = OSPEEDR;
temp &= ~(OSPEEDR_MASK << (conf->pin * 2u));
temp |= (GPIO_SPEED_FREQ_LOW << (conf->pin * 2u));
OSPEEDR = temp;
/* ... */
}
/* ... */
}
ldr r2, [r0, #0]
push {r4, r5, lr}
cmp r2, #15
bhi.n 80001da <GPIO_Init+0x42>
ldrb r3, [r0, #4]
cmp r3, #1
bhi.n 80001da <GPIO_Init+0x42>
bne.n 80001c4 <GPIO_Init+0x2c>
movs r4, #3
lsls r2, r2, #1
lsls r4, r2
ldr r5, [pc, #44]
ldr r1, [r5, #0]
bics r1, r4
movs r4, r3
str r1, [r5, #0]
if pin is greater than 15, branch to the end (invalid pin check)

## Slide 17
Inefficiencies in HAL
typedef struct {
uint32_t pin;
GPIO_Modes mode;
} GPIO_InitStruct;
void GPIO_Init(GPIO_InitStruct* conf) {
uint32_t temp;
/* check the values */
if (!IS_GPIO_PIN(conf->pin)) { return; }
if (!IS_GPIO_MODE(conf->mode)) { return; }
/* configure the GPIO based on the settings */
if (conf->mode == GPIO_MODE_OUTPUT) {
temp = OSPEEDR;
temp &= ~(OSPEEDR_MASK << (conf->pin * 2u));
temp |= (GPIO_SPEED_FREQ_LOW << (conf->pin * 2u));
OSPEEDR = temp;
/* ... */
}
/* ... */
}
ldr r2, [r0, #0]
push {r4, r5, lr}
cmp r2, #15
bhi.n 80001da <GPIO_Init+0x42>
ldrb r3, [r0, #4]
cmp r3, #1
bhi.n 80001da <GPIO_Init+0x42>
bne.n 80001c4 <GPIO_Init+0x2c>
movs r4, #3
lsls r2, r2, #1
lsls r4, r2
ldr r5, [pc, #44]
ldr r1, [r5, #0]
bics r1, r4
movs r4, r3
str r1, [r5, #0]
if mode is greater than 1, branch to the end (invalid mode check)

## Slide 18
Inefficiencies in HAL
typedef struct {
uint32_t pin;
GPIO_Modes mode;
} GPIO_InitStruct;
void GPIO_Init(GPIO_InitStruct* conf) {
uint32_t temp;
/* check the values */
if (!IS_GPIO_PIN(conf->pin)) { return; }
if (!IS_GPIO_MODE(conf->mode)) { return; }
/* configure the GPIO based on the settings */
if (conf->mode == GPIO_MODE_OUTPUT) {
temp = OSPEEDR;
temp &= ~(OSPEEDR_MASK << (conf->pin * 2u));
temp |= (GPIO_SPEED_FREQ_LOW << (conf->pin * 2u));
OSPEEDR = temp;
/* ... */
}
/* ... */
}
ldr r2, [r0, #0]
push {r4, r5, lr}
cmp r2, #15
bhi.n 80001da <GPIO_Init+0x42>
ldrb r3, [r0, #4]
cmp r3, #1
bhi.n 80001da <GPIO_Init+0x42>
bne.n 80001c4 <GPIO_Init+0x2c>
movs r4, #3
lsls r2, r2, #1
lsls r4, r2
ldr r5, [pc, #44]
ldr r1, [r5, #0]
bics r1, r4
movs r4, r3
str r1, [r5, #0]
if mode is not 1, branch to configure pin for input mode

## Slide 19
Inefficiencies in HAL
typedef struct {
uint32_t pin;
GPIO_Modes mode;
} GPIO_InitStruct;
void GPIO_Init(GPIO_InitStruct* conf) {
uint32_t temp;
/* check the values */
if (!IS_GPIO_PIN(conf->pin)) { return; }
if (!IS_GPIO_MODE(conf->mode)) { return; }
/* configure the GPIO based on the settings */
if (conf->mode == GPIO_MODE_OUTPUT) {
temp = OSPEEDR;
temp &= ~(OSPEEDR_MASK << (conf->pin * 2u));
temp |= (GPIO_SPEED_FREQ_LOW << (conf->pin * 2u));
OSPEEDR = temp;
/* ... */
}
/* ... */
}
ldr r2, [r0, #0]
push {r4, r5, lr}
cmp r2, #15
bhi.n 80001da <GPIO_Init+0x42>
ldrb r3, [r0, #4]
cmp r3, #1
bhi.n 80001da <GPIO_Init+0x42>
bne.n 80001c4 <GPIO_Init+0x2c>
movs r4, #3
lsls r2, r2, #1
lsls r4, r2
ldr r5, [pc, #44]
ldr r1, [r5, #0]
bics r1, r4
movs r4, r3
str r1, [r5, #0]
prepare mask value for OSPEEDR (3)

## Slide 20
Inefficiencies in HAL
typedef struct {
uint32_t pin;
GPIO_Modes mode;
} GPIO_InitStruct;
void GPIO_Init(GPIO_InitStruct* conf) {
uint32_t temp;
/* check the values */
if (!IS_GPIO_PIN(conf->pin)) { return; }
if (!IS_GPIO_MODE(conf->mode)) { return; }
/* configure the GPIO based on the settings */
if (conf->mode == GPIO_MODE_OUTPUT) {
temp = OSPEEDR;
temp &= ~(OSPEEDR_MASK << (conf->pin * 2u));
temp |= (GPIO_SPEED_FREQ_LOW << (conf->pin * 2u));
OSPEEDR = temp;
/* ... */
}
/* ... */
}
ldr r2, [r0, #0]
push {r4, r5, lr}
cmp r2, #15
bhi.n 80001da <GPIO_Init+0x42>
ldrb r3, [r0, #4]
cmp r3, #1
bhi.n 80001da <GPIO_Init+0x42>
bne.n 80001c4 <GPIO_Init+0x2c>
movs r4, #3
lsls r2, r2, #1
lsls r4, r2
ldr r5, [pc, #44]
ldr r1, [r5, #0]
bics r1, r4
movs r4, r3
str r1, [r5, #0]
shift pin value left by 1 bit (pin * 2)

## Slide 21
Inefficiencies in HAL
typedef struct {
uint32_t pin;
GPIO_Modes mode;
} GPIO_InitStruct;
void GPIO_Init(GPIO_InitStruct* conf) {
uint32_t temp;
/* check the values */
if (!IS_GPIO_PIN(conf->pin)) { return; }
if (!IS_GPIO_MODE(conf->mode)) { return; }
/* configure the GPIO based on the settings */
if (conf->mode == GPIO_MODE_OUTPUT) {
temp = OSPEEDR;
temp &= ~(OSPEEDR_MASK << (conf->pin * 2u));
temp |= (GPIO_SPEED_FREQ_LOW << (conf->pin * 2u));
OSPEEDR = temp;
/* ... */
}
/* ... */
}
ldr r2, [r0, #0]
push {r4, r5, lr}
cmp r2, #15
bhi.n 80001da <GPIO_Init+0x42>
ldrb r3, [r0, #4]
cmp r3, #1
bhi.n 80001da <GPIO_Init+0x42>
bne.n 80001c4 <GPIO_Init+0x2c>
movs r4, #3
lsls r2, r2, #1
lsls r4, r2
ldr r5, [pc, #44]
ldr r1, [r5, #0]
bics r1, r4
movs r4, r3
str r1, [r5, #0]
shift mask value left by (pin * 2) positions

## Slide 22
Inefficiencies in HAL
typedef struct {
uint32_t pin;
GPIO_Modes mode;
} GPIO_InitStruct;
void GPIO_Init(GPIO_InitStruct* conf) {
uint32_t temp;
/* check the values */
if (!IS_GPIO_PIN(conf->pin)) { return; }
if (!IS_GPIO_MODE(conf->mode)) { return; }
/* configure the GPIO based on the settings */
if (conf->mode == GPIO_MODE_OUTPUT) {
temp = OSPEEDR;
temp &= ~(OSPEEDR_MASK << (conf->pin * 2u));
temp |= (GPIO_SPEED_FREQ_LOW << (conf->pin * 2u));
OSPEEDR = temp;
/* ... */
}
/* ... */
}
ldr r2, [r0, #0]
push {r4, r5, lr}
cmp r2, #15
bhi.n 80001da <GPIO_Init+0x42>
ldrb r3, [r0, #4]
cmp r3, #1
bhi.n 80001da <GPIO_Init+0x42>
bne.n 80001c4 <GPIO_Init+0x2c>
movs r4, #3
lsls r2, r2, #1
lsls r4, r2
ldr r5, [pc, #44]
ldr r1, [r5, #0]
bics r1, r4
movs r4, r3
str r1, [r5, #0]
load address of OSPEEDR into r5

## Slide 23
Inefficiencies in HAL
typedef struct {
uint32_t pin;
GPIO_Modes mode;
} GPIO_InitStruct;
void GPIO_Init(GPIO_InitStruct* conf) {
uint32_t temp;
/* check the values */
if (!IS_GPIO_PIN(conf->pin)) { return; }
if (!IS_GPIO_MODE(conf->mode)) { return; }
/* configure the GPIO based on the settings */
if (conf->mode == GPIO_MODE_OUTPUT) {
temp = OSPEEDR;
temp &= ~(OSPEEDR_MASK << (conf->pin * 2u));
temp |= (GPIO_SPEED_FREQ_LOW << (conf->pin * 2u));
OSPEEDR = temp;
/* ... */
}
/* ... */
}
ldr r2, [r0, #0]
push {r4, r5, lr}
cmp r2, #15
bhi.n 80001da <GPIO_Init+0x42>
ldrb r3, [r0, #4]
cmp r3, #1
bhi.n 80001da <GPIO_Init+0x42>
bne.n 80001c4 <GPIO_Init+0x2c>
movs r4, #3
lsls r2, r2, #1
lsls r4, r2
ldr r5, [pc, #44]
ldr r1, [r5, #0]
bics r1, r4
movs r4, r3
str r1, [r5, #0]
load current OSPEEDR value into r1

## Slide 24
Inefficiencies in HAL
typedef struct {
uint32_t pin;
GPIO_Modes mode;
} GPIO_InitStruct;
void GPIO_Init(GPIO_InitStruct* conf) {
uint32_t temp;
/* check the values */
if (!IS_GPIO_PIN(conf->pin)) { return; }
if (!IS_GPIO_MODE(conf->mode)) { return; }
/* configure the GPIO based on the settings */
if (conf->mode == GPIO_MODE_OUTPUT) {
temp = OSPEEDR;
temp &= ~(OSPEEDR_MASK << (conf->pin * 2u));
temp |= (GPIO_SPEED_FREQ_LOW << (conf->pin * 2u));
OSPEEDR = temp;
/* ... */
}
/* ... */
}
ldr r2, [r0, #0]
push {r4, r5, lr}
cmp r2, #15
bhi.n 80001da <GPIO_Init+0x42>
ldrb r3, [r0, #4]
cmp r3, #1
bhi.n 80001da <GPIO_Init+0x42>
bne.n 80001c4 <GPIO_Init+0x2c>
movs r4, #3
lsls r2, r2, #1
lsls r4, r2
ldr r5, [pc, #44]
ldr r1, [r5, #0]
bics r1, r4
movs r4, r3
str r1, [r5, #0]
clear the two bits for the pin in OSPEEDR

## Slide 25
Inefficiencies in HAL
typedef struct {
uint32_t pin;
GPIO_Modes mode;
} GPIO_InitStruct;
void GPIO_Init(GPIO_InitStruct* conf) {
uint32_t temp;
/* check the values */
if (!IS_GPIO_PIN(conf->pin)) { return; }
if (!IS_GPIO_MODE(conf->mode)) { return; }
/* configure the GPIO based on the settings */
if (conf->mode == GPIO_MODE_OUTPUT) {
temp = OSPEEDR;
temp &= ~(OSPEEDR_MASK << (conf->pin * 2u));
temp |= (GPIO_SPEED_FREQ_LOW << (conf->pin * 2u));
OSPEEDR = temp;
/* ... */
}
/* ... */
}
ldr r2, [r0, #0]
push {r4, r5, lr}
cmp r2, #15
bhi.n 80001da <GPIO_Init+0x42>
ldrb r3, [r0, #4]
cmp r3, #1
bhi.n 80001da <GPIO_Init+0x42>
bne.n 80001c4 <GPIO_Init+0x2c>
movs r4, #3
lsls r2, r2, #1
lsls r4, r2
ldr r5, [pc, #44]
ldr r1, [r5, #0]
bics r1, r4
movs r4, r3
str r1, [r5, #0]
GPIO_SPEED_FREQ_LOW is 0 -> optimized

## Slide 26
Inefficiencies in HAL
typedef struct {
uint32_t pin;
GPIO_Modes mode;
} GPIO_InitStruct;
void GPIO_Init(GPIO_InitStruct* conf) {
uint32_t temp;
/* check the values */
if (!IS_GPIO_PIN(conf->pin)) { return; }
if (!IS_GPIO_MODE(conf->mode)) { return; }
/* configure the GPIO based on the settings */
if (conf->mode == GPIO_MODE_OUTPUT) {
temp = OSPEEDR;
temp &= ~(OSPEEDR_MASK << (conf->pin * 2u));
temp |= (GPIO_SPEED_FREQ_LOW << (conf->pin * 2u));
OSPEEDR = temp;
/* ... */
}
/* ... */
}
ldr r2, [r0, #0]
push {r4, r5, lr}
cmp r2, #15
bhi.n 80001da <GPIO_Init+0x42>
ldrb r3, [r0, #4]
cmp r3, #1
bhi.n 80001da <GPIO_Init+0x42>
bne.n 80001c4 <GPIO_Init+0x2c>
movs r4, #3
lsls r2, r2, #1
lsls r4, r2
ldr r5, [pc, #44]
ldr r1, [r5, #0]
bics r1, r4
movs r4, r3
str r1, [r5, #0]
store the modified OSPEEDR value back

## Slide 27
Functions

## Slide 28
Functions

## Slide 29
Functions

## Slide 30
Functions

## Slide 31
Functions

## Slide 32
Building Layers of Abstractions
Take the original C code, modify as little as possible, focusing only on the abstraction in question.
Compare the binary size, compilation time (generated code) and the runtime performance (analytically now, empirically probably only at the end).
C code

## Slide 33
Building Layers of Abstractions
Take the original C code, modify as little as possible, focusing only on the abstraction in question.
Compare the binary size, compilation time (generated code) and the runtime performance (analytically now, empirically probably only at the end).
C code
C++ code

## Slide 34
Encapsulation

## Slide 35
Encapsulation

## Slide 36
Encapsulation
(basic)
class CRegister {
private:
const std::uint32_t m_address;
public:
CRegister (std::uint32_t address) : m_address(address) { }
void set (std::uint32_t val) const {
*(reinterpret_cast<volatile std::uint32_t *>(m_address)) = val;
}
/* ... */
};

## Slide 37
Encapsulation
(basic)
class CRegister {
private:
const std::uint32_t m_address;
public:
CRegister (std::uint32_t address) : m_address(address) { }
void set (std::uint32_t val) const {
*(reinterpret_cast<volatile std::uint32_t *>(m_address)) = val;
}
/* ... */
};

## Slide 38
Encapsulation
(basic)
class CRegister {
private:
const std::uint32_t m_address;
public:
CRegister (std::uint32_t address) : m_address(address) { }
void set (std::uint32_t val) const {
*(reinterpret_cast<volatile std::uint32_t *>(m_address)) = val;
}
/* ... */
};

## Slide 39
Encapsulation
(basic)
class CRegister {
private:
const std::uint32_t m_address;
public:
CRegister (std::uint32_t address) : m_address(address) { }
void set (std::uint32_t val) const {
*(reinterpret_cast<volatile std::uint32_t *>(m_address)) = val;
}
/* ... */
};

## Slide 40
Encapsulation
(basic)
class CRegister {
private:
const std::uint32_t m_address;
public:
CRegister (std::uint32_t address) : m_address(address) { }
void set (std::uint32_t val) const {
*(reinterpret_cast<volatile std::uint32_t *>(m_address)) = val;
}
/* ... */
};
temp = OSPEEDR;
temp &= ~(OSPEEDR_MASK << (conf->pin * 2u));
temp |= (conf->speed << (conf->pin * 2u));
OSPEEDR = temp;

## Slide 41
Encapsulation

## Slide 42
Encapsulation
(basic)
class CModeRegister {
private:
const CRegister m_register { 0x48000000 };
inline std::uint32_t calculate_value (std::uint32_t pin, GPIO_Modes mode) {
return (mode & GPIO_MODE) << (pin * 2);
}
inline std::uint32_t calculate_bitmask (std::uint32_t pin) {
return MODER_MASK << (pin * 2);
}
public:
inline void set_mode (std::uint32_t pin, GPIO_Modes mode) {
m_register.set(calculate_value(pin, mode), calculate_bitmask(pin));
}
};

## Slide 43
Encapsulation
(basic)
class CModeRegister {
private:
const CRegister m_register { 0x48000000 };
inline std::uint32_t calculate_value (std::uint32_t pin, GPIO_Modes mode) {
return (mode & GPIO_MODE) << (pin * 2);
}
inline std::uint32_t calculate_bitmask (std::uint32_t pin) {
return MODER_MASK << (pin * 2);
}
public:
inline void set_mode (std::uint32_t pin, GPIO_Modes mode) {
m_register.set(calculate_value(pin, mode), calculate_bitmask(pin));
}
};

## Slide 44
Encapsulation
(basic)
class CModeRegister {
private:
const CRegister m_register { 0x48000000 };
inline std::uint32_t calculate_value (std::uint32_t pin, GPIO_Modes mode) {
return (mode & GPIO_MODE) << (pin * 2);
}
inline std::uint32_t calculate_bitmask (std::uint32_t pin) {
return MODER_MASK << (pin * 2);
}
public:
inline void set_mode (std::uint32_t pin, GPIO_Modes mode) {
m_register.set(calculate_value(pin, mode), calculate_bitmask(pin));
}
};

## Slide 45
Encapsulation
(basic)
class CModeRegister {
private:
const CRegister m_register { 0x48000000 };
inline std::uint32_t calculate_value (std::uint32_t pin, GPIO_Modes mode) {
return (mode & GPIO_MODE) << (pin * 2);
}
inline std::uint32_t calculate_bitmask (std::uint32_t pin) {
return MODER_MASK << (pin * 2);
}
public:
inline void set_mode (std::uint32_t pin, GPIO_Modes mode) {
m_register.set(calculate_value(pin, mode), calculate_bitmask(pin));
}
};

## Slide 46
Encapsulation
(basic)
class CModeRegister {
private:
const CRegister m_register { 0x48000000 };
inline std::uint32_t calculate_value (std::uint32_t pin, GPIO_Modes mode) {
return (mode & GPIO_MODE) << (pin * 2);
}
inline std::uint32_t calculate_bitmask (std::uint32_t pin) {
return MODER_MASK << (pin * 2);
}
public:
inline void set_mode (std::uint32_t pin, GPIO_Modes mode) {
m_register.set(calculate_value(pin, mode), calculate_bitmask(pin));
}
};
temp = OSPEEDR;
temp &= ~(OSPEEDR_MASK << (conf->pin * 2u));
temp |= (conf->speed << (conf->pin * 2u));
OSPEEDR = temp;

## Slide 47
Encapsulation
(basic)
void GPIO_Init(GPIO_InitStruct* conf) {
/* ... */
if (conf->mode == GPIO_MODE_OUTPUT) {
COutputSpeedRegister ospeedr {};
ospeedr.set_speed(conf->pin, conf->speed);
COutputTypeRegister otyper {};
otyper.set_type(conf->pin, conf->type);
}
CModeRegister moder {};
moder.set_mode(conf->pin, conf->mode);
/* ... */
}
void GPIO_Init(GPIO_InitStruct* conf) {
/* ... */
if (conf->mode == GPIO_MODE_OUTPUT) {
temp = OSPEEDR;
temp &= ~(OSPEEDR_MASK << (conf->pin * 2u));
temp |= (conf->speed << (conf->pin * 2u));
OSPEEDR = temp;
temp = OTYPER;
temp &= ~(OTYPER_MASK << conf->pin);
temp |= (((conf->type & GPIO_OUTPUT_TYPE) >> 4u)
<< conf->pin);
OTYPER = temp;
}
temp = MODER;
temp &= ~(MODER_MASK << (conf->pin * 2u));
temp |= ((conf->mode & GPIO_MODE) << (conf->pin * 2u));
MODER = temp;
/* ... */
}

## Slide 48
Encapsulation
(basic)
Compiles to the same binary.
TODO : compilation time?

## Slide 49
Encapsulation
(static)
void GPIO_Init(GPIO_InitStruct* conf) {
/* check the values */
if (!IS_GPIO_PIN(conf->pin)) { return; }
if (!IS_GPIO_MODE(conf->mode)) { return; }
/* configure the GPIO based on the settings */
if (conf->mode == GPIO_MODE_OUTPUT) {
COutputSpeedRegister::set_speed(conf->pin, conf->speed);
COutputTypeRegister::set_type(conf->pin, conf->type);
}
CModeRegister::set_mode(conf->pin, conf->mode);
/* ... */
}

## Slide 50
Encapsulation
(static)
class CModeRegister {
private:
static inline const CRegister m_register { 0x48000000 };
static inline std::uint32_t calculate_value (std::uint32_t pin, GPIO_Modes mode) {
return (mode & GPIO_MODE) << (pin * 2);
}
static inline std::uint32_t calculate_bitmask (std::uint32_t pin) {
return MODER_MASK << (pin * 2);
}
public:
static inline void set_mode (std::uint32_t pin, GPIO_Modes mode) {
m_register.set(calculate_value(pin, mode), calculate_bitmask(pin));
}
};

## Slide 51
Encapsulation
(static)
Binary size increase… why?

## Slide 52
Encapsulation
(static)
_GLOBAL__sub_I__Z9GPIO_InitP15GPIO_InitStruct
Objects with static storage duration need to be initialized before the main function starts executing.
This function initializes the static CRegister objects and loads the values used in the static member functions of the register classes.
Does not affect runtime performance, as it executes before the main function, but it increases binary size.

## Slide 53
template <std::uint32_t address>
class CRegister {
public:
void set (std::uint32_t val) const {
*(reinterpret_cast<volatile std::uint32_t *>(address)) = val;
}
/* ... */
};
Encapsulation
(static & template)

## Slide 54
class CModeRegister {
private:
static inline const CRegister<0x48000000> m_register { };
/* ... */
};
Encapsulation
(static & template)
class CModeRegister {
private:
static inline const CRegister m_register { 0x48000000 };
/* ... */
};

## Slide 55
Encapsulation
(static & template)
Binary size is back to the original.
Each CRegister instance is fully defined at compile time.
No global state that needs to be explicitly initialized before main.
Compiler can better optimize the code at compile time.

## Slide 56
Encapsulation
(static & template)

## Slide 57
Inheritance
class COutputSpeedRegister : public CRegister<0x48000008> {
private:
static inline std::uint32_t calculate_value (std::uint32_t pin, GPIO_Output_Speeds speed) {
return speed << (pin * 2);
}
static inline std::uint32_t calculate_bitmask (std::uint32_t pin) {
return OSPEEDR_MASK << (pin * 2);
}
public:
static inline void set_speed (std::uint32_t pin, GPIO_Output_Speeds speed) {
set(calculate_value(pin, speed), calculate_bitmask(pin));
}
};

## Slide 58
Inheritance
Compiles to the same binary.

## Slide 59
Inheritance

## Slide 60
Moving Higher
Microcontroller
Peripheral

## Slide 61
Moving Higher
HAL
External Peripheral Interface
STM32
ESP32
PIC32
Microcontroller
Peripheral

## Slide 62
Moving Higher
HAL
External Peripheral Interface
STM32
ESP32
PIC32
Microcontroller
Peripheral

## Slide 63
Moving Higher
HAL
External Peripheral Interface
STM32
ESP32
PIC32
Microcontroller
Peripheral
Dynamic Polymorphism
interfaces
realizations

## Slide 64
Dynamic Polymorphism
class IPin {
public:
virtual void set () = 0;
virtual void reset () = 0;
};

## Slide 65
Dynamic Polymorphism
class CLed {
private:
bool m_state { false };
IPin* m_pin { nullptr };
public:
CLed () = delete;
CLed (IPin* pin) : m_pin(pin) {
m_pin->reset();
}
/* ... */
};

## Slide 66
Dynamic Polymorphism
class CPin : public IPin {
private:
std::uint8_t m_pin { 0 };
public:
CPin () = delete;
CPin (std::uint8_t pin) : m_pin(pin) {}
void set () override {
CBitSetResetRegister::set_pin(m_pin);
}
void reset () override {
CBitSetResetRegister::reset_pin(m_pin);
}
};

## Slide 67
Dynamic Polymorphism

## Slide 68
Dynamic Polymorphism
To RTTI, or not to RTTI...
Run-Time Type Information
  _type_info sections in the binary
  Necessary for:
      typeid
      dynamic_cast

## Slide 69
Dynamic Polymorphism
For statically allocated objects, the compiler can often determine the type at compile-time.
-> no virtual function calls (de-virtualization)
CPin pin { GPIO_PIN_6 };
CLed led { &pin };
while (true) {
led.toggle();
delay(1000);
}

## Slide 70
Dynamic Polymorphism
without de-virtualization
080001b0 <_ZN4CPin3setEv>: ...
08000198 <_ZN4CPin5resetEv>: ...

## Slide 71
Dynamic Polymorphism
without de-virtualization
080001b0 <_ZN4CPin3setEv>: ...
08000198 <_ZN4CPin5resetEv>: ...
0x08000258 : 0x080001b1
0x0800025c : 0x08000199
CLed vtable

## Slide 72
Dynamic Polymorphism
without de-virtualization
080001b0 <_ZN4CPin3setEv>: ...
08000198 <_ZN4CPin5resetEv>: ...
0x08000258 : 0x080001b1
0x0800025c : 0x08000199
CLed vtable
<main>:
push {r0, r1, r2, lr}
ldr r3, [pc, #28] ; (80001e4 <main+0x20>)
mov r2, sp
str r3, [sp, #0]
movs r3, #6
strb r3, [r2, #4]
ldr r3, [sp, #0]
mov r0, sp
ldr r3, [r3, #0]
blx r3
ldr r3, [sp, #0]
mov r0, sp
ldr r3, [r3, #4]
blx r3
b.n 80001d0 <main+0xc>
Nop ; (mov r8, r8)
.word 0x08000258

## Slide 73
Dynamic Polymorphism
without de-virtualization
<main>:
push {r0, r1, r2, lr}
ldr r3, [pc, #28] ; (80001e4 <main+0x20>)
mov r2, sp
str r3, [sp, #0]
movs r3, #6
strb r3, [r2, #4]
ldr r3, [sp, #0]
mov r0, sp
ldr r3, [r3, #0]
blx r3
ldr r3, [sp, #0]
mov r0, sp
ldr r3, [r3, #4]
blx r3
b.n 80001d0 <main+0xc>
Nop ; (mov r8, r8)
.word 0x08000258
080001b0 <_ZN4CPin3setEv>: ...
08000198 <_ZN4CPin5resetEv>: ...
0x08000258 : 0x080001b1
0x0800025c : 0x08000199
CLed vtable
Load the vtable address in r3.

## Slide 74
Dynamic Polymorphism
without de-virtualization
<main>:
push {r0, r1, r2, lr}
ldr r3, [pc, #28] ; (80001e4 <main+0x20>)
mov r2, sp
str r3, [sp, #0]
movs r3, #6
strb r3, [r2, #4]
ldr r3, [sp, #0]
mov r0, sp
ldr r3, [r3, #0]
blx r3
ldr r3, [sp, #0]
mov r0, sp
ldr r3, [r3, #4]
blx r3
b.n 80001d0 <main+0xc>
Nop ; (mov r8, r8)
.word 0x08000258
080001b0 <_ZN4CPin3setEv>: ...
08000198 <_ZN4CPin5resetEv>: ...
0x08000258 : 0x080001b1
0x0800025c : 0x08000199
CLed vtable
Load the address of the reset method from the vtable into r3.

## Slide 75
Dynamic Polymorphism
without de-virtualization
<main>:
push {r0, r1, r2, lr}
ldr r3, [pc, #28] ; (80001e4 <main+0x20>)
mov r2, sp
str r3, [sp, #0]
movs r3, #6
strb r3, [r2, #4]
ldr r3, [sp, #0]
mov r0, sp
ldr r3, [r3, #0]
blx r3
ldr r3, [sp, #0]
mov r0, sp
ldr r3, [r3, #4]
blx r3
b.n 80001d0 <main+0xc>
Nop ; (mov r8, r8)
.word 0x08000258
080001b0 <_ZN4CPin3setEv>: ...
08000198 <_ZN4CPin5resetEv>: ...
0x08000258 : 0x080001b1
0x0800025c : 0x08000199
CLed vtable
Call the reset method via the address in r3.

## Slide 76
Dynamic Polymorphism
without de-virtualization
<main>:
push {r0, r1, r2, lr}
ldr r3, [pc, #28] ; (80001e4 <main+0x20>)
mov r2, sp
str r3, [sp, #0]
movs r3, #6
strb r3, [r2, #4]
ldr r3, [sp, #0]
mov r0, sp
ldr r3, [r3, #0]
blx r3
ldr r3, [sp, #0]
mov r0, sp
ldr r3, [r3, #4]
blx r3
b.n 80001d0 <main+0xc>
Nop ; (mov r8, r8)
.word 0x08000258
080001b0 <_ZN4CPin3setEv>: ...
08000198 <_ZN4CPin5resetEv>: ...
0x08000258 : 0x080001b1
0x0800025c : 0x08000199
CLed vtable
Load the address of the set method from the vtable into r3.

## Slide 77
Dynamic Polymorphism
without de-virtualization
<main>:
push {r0, r1, r2, lr}
ldr r3, [pc, #28] ; (80001e4 <main+0x20>)
mov r2, sp
str r3, [sp, #0]
movs r3, #6
strb r3, [r2, #4]
ldr r3, [sp, #0]
mov r0, sp
ldr r3, [r3, #0]
blx r3
ldr r3, [sp, #0]
mov r0, sp
ldr r3, [r3, #4]
blx r3
b.n 80001d0 <main+0xc>
Nop ; (mov r8, r8)
.word 0x08000258
080001b0 <_ZN4CPin3setEv>: ...
08000198 <_ZN4CPin5resetEv>: ...
0x08000258 : 0x080001b1
0x0800025c : 0x08000199
CLed vtable
Call the set method via the address in r3.

## Slide 78
Recap
HAL
External Peripheral Interface
STM32
ESP32
PIC32
Microcontroller
Peripheral

## Slide 79
Static Polymorphism
HAL
External Peripheral Interface
STM32
ESP32
PIC32
Microcontroller
Peripheral
Static Polymorphism
Interfaces using concepts
Implementations that satisfy the requirements

## Slide 80
Static Polymorphism
template <typename T>
concept IPin = requires (T pin) {
{ pin.set() } -> std::same_as<void>;
{ pin.reset() } -> std::same_as<void>;
};

## Slide 81
Static Polymorphism
template <IPin TPin>
class CLed {
private:
bool m_state { false };
TPin* m_pin { nullptr };
public:
CLed () = delete;
CLed (TPin* pin) : m_pin(pin) {
m_pin->reset();
}
/* ... */
};

## Slide 82
Static Polymorphism
class CPin {
private:
std::uint8_t m_pin { 0 };
public:
CPin () = delete;
CPin (std::uint8_t pin) : m_pin(pin) {}
void set () override {
CBitSetResetRegister::set_pin(m_pin);
}
void reset () override {
CBitSetResetRegister::reset_pin(m_pin);
}
};
static_assert(IPin<CPin>); // optional

## Slide 83
Static Polymorphism
Compiles to the same binary.

## Slide 84
Polymorphism

## Slide 85
Polymorphism

## Slide 86
Inefficiencies in HAL
Runtime bitmask calculations
Runtime branching
Function calls
Runtime input validation

## Slide 87
Runtime bitmask calculations
Runtime branching
Function calls
Runtime input validation
Inefficiencies in HAL

## Slide 88
Setup
STM32
ANALOG
ANALOG
GPIO
PWM

## Slide 89
Modules
Timer
Clock & Oscillator
SysTick
UART
ADC
GPIO
C

## Slide 90
Modules
Timer
Clock & Oscillator
SysTick
UART
ADC
GPIO
Delays (us, ms)
PWM
Time measurement
Communication
with PC
Analog input
LEDs
Clock configuration
C

## Slide 91
Modules
Timer
Clock & Oscillator
SysTick
UART
ADC
GPIO
C++
C
Delays (us, ms)
PWM
Time measurement
Communication
with PC
Analog input
LEDs
Clock configuration

## Slide 92
This is about the “special” cases where the hardware is known, which is quite common for embedded systems.
I did not replace the HAL given by the manufacturer, I extended it.
The same techniques can be used in any other application as well, if the circumstances allow it.
These are no guidelines or rules.
Notes

## Slide 93
Enumerations
enum class modes : std::uint32_t {
input = 0b00,
output = 0b01,
alt_func = 0b10,
analog = 0b11
};
enum class ports : std::uint8_t {
port_f,
port_d,
port_c,
port_b,
port_a
};
Enumerations
  Not plain integers anymore
  No implicit conversions between enum values and integral types
      Explicit static_cast required
      Harder to misuse accidentally

## Slide 94
Concepts
template <modes mode>
concept is_valid_mode = (
(mode == modes::input) ||
(mode == modes::output) ||
(mode == modes::alt_func) ||
(mode == modes::analog)
);
template <pins pin>
concept is_valid_pin = (
is_valid_low_pin<pin> || is_valid_high_pin<pin>
);
template <pins... pin>
concept are_valid_pins = (is_valid_pin<pin> && ...);

## Slide 95
Immediate Functions
template <modes mode, pins... pin>
requires (are_valid_pins<pin ...> && is_valid_mode<mode>)
consteval std::uint32_t moder_value () {
return (... | (static_cast<std::uint32_t>(mode) <<
(static_cast<std::uint32_t>(pin) * 2)));
}
template <pins... pin>
requires (are_valid_pins<pin ...>)
consteval std::uint32_t moder_bitmask () {
return (... | (GPIO_MODER_MODER0 <<
(static_cast<std::uint32_t>(pin) * 2)));
}

## Slide 96
Compile-time Branching
template <GpioInitConfig conf, pins... pin>
requires (is_valid_gpio_config<conf> && are_valid_pins<pin...>)
static inline void configure_pins() {
static_assert((sizeof...(pin) > 0), "No pins provided.");
if constexpr ((conf.mode == modes::output) || (conf.mode == modes::alt_func)) {
/* ... */
}
if constexpr (conf.mode != modes::analog) {
/* ... */
}
if constexpr (conf.mode == modes::alt_func) {
/* ... */
}
/* ... */
}

## Slide 97
Result
Compile time parameter validation
Compile time bitmask calculations
Compile time branching
Complex functions -> couple of register operations

## Slide 98
Result

## Slide 99
WARNING
Compile time parameter validation
Compile time bitmask calculations
Compile time branching
Complex functions -> couple of register operations