## Slide 1: Balancing Efficiency and Flexibility
Cost of Abstractions in Embedded Systems Marcell Juhasz
Notes: Hello Everyone! I am Marcell Juhasz. Welcome to my presentation about the cost of abstractions in embedded systems.

## Slide 2
whoami
Marcell Juhasz
github.com/juhaszmarcell96
linkedin.com/in/juhaszmarcell
marcell.juhasz96@gmail.com
Zühlke Engineering (Austria) GmbH
Rivergate, Handelskai 92
1200, Vienna, Austria
wien@zuehlke.com
+43 1 205 11 6800

## Slide 3
Motivation
C is dominant in the embedded world
  direct interaction with hardware
  flexible
  robust
  efficient
Common opinions:
  C is as efficient as it gets
  abstraction = less efficient software
  C++ comes with inherent runtime overhead

## Slide 4
Overview
Hardware Abstraction Layer
Encapsulation
Inheritance
Polymorphism
+
Template Metaprogramming
Concepts
Constant Expressions
Immediate Functions
Parameter Pack and Fold Expressions
Constexpr If Statements

## Slide 5
source code
Methodology
cross-compilation
arm-none-eabi 10.3.1
STM32F030CC
objdump
st-flash
compilation time
runtime performance (analytical)
runtime performance (empirical)
binary size
binary
analysis of disassembled binary
measurement of runtime performance

## Slide 6
Base Firmware
Absolute minimal embedded project:
  Startup script:
      Defines the vector table
      Sets stack pointer
      Copies data section from flash to RAM
      Initializes uninitialized global and static variables to zero
      Calls static constructors
      Calls main()
  Linker Script: specifies the memory layout
  Main function:
      Entry point of the firmware
      Consists of a single, empty infinite loop
2092 bytes
  text: 524 bytes
  data: 0 bytes
  bss: 1568 bytes

## Slide 7
Inefficiencies in HAL
Enums are basically integers with no value restrictions
Runtime branching based on input parameters
Runtime bitmask calculations
C++ support = extern “C”
typedef struct {
uint32_t pin;
GPIO_Modes mode;
} GPIO_InitStruct;
void GPIO_Init(GPIO_InitStruct* conf) {
uint32_t temp;
/* check the values */
if (!IS_GPIO_PIN(conf->pin)) { return; }
if (!IS_GPIO_MODE(conf->mode)) { return; }
/* configure the GPIO based on the settings */
if (conf->mode == GPIO_MODE_OUTPUT) {
temp = OSPEEDR;
temp &= ~(OSPEEDR_MASK << (conf->pin * 2u));
temp |= (GPIO_SPEED_FREQ_LOW << (conf->pin * 2u));
OSPEEDR = temp;
/* ... */
}
/* ... */
}

## Slide 8
Inefficiencies in HAL
int main (void) {
GPIO_InitStruct conf = { 0 };
conf.pin = GPIO_PIN_6;
conf.mode = GPIO_MODE_INPUT;
GPIO_Init(&conf) ;
while (1) { }
}
<main>:
movs r3, #6
push {r0, r1, r2, lr}
str r3, [sp, #0]
mov r0, sp
subs r3, #5
str r3, [sp, #4]
bl 8000198 <GPIO_Init>
b.n 80001f4 <main+0x10>
set up the pin value for GPIO_PIN_6 (value 6)

## Slide 9
Inefficiencies in HAL
int main (void) {
GPIO_InitStruct conf = { 0 };
conf.pin = GPIO_PIN_6;
conf.mode = GPIO_MODE_INPUT;
GPIO_Init(&conf) ;
while (1) { }
}
<main>:
movs r3, #6
push {r0, r1, r2, lr}
str r3, [sp, #0]
mov r0, sp
subs r3, #5
str r3, [sp, #4]
bl 8000198 <GPIO_Init>
b.n 80001f4 <main+0x10>
prepare for calling a function by saving the current state

## Slide 10
Inefficiencies in HAL
int main (void) {
GPIO_InitStruct conf = { 0 };
conf.pin = GPIO_PIN_6;
conf.mode = GPIO_MODE_INPUT;
GPIO_Init(&conf) ;
while (1) { }
}
<main>:
movs r3, #6
push {r0, r1, r2, lr}
str r3, [sp, #0]
mov r0, sp
subs r3, #5
str r3, [sp, #4]
bl 8000198 <GPIO_Init>
b.n 80001f4 <main+0x10>
store the pin value in the GPIO_InitStruct structure on the stack

## Slide 11
Inefficiencies in HAL
int main (void) {
GPIO_InitStruct conf = { 0 };
conf.pin = GPIO_PIN_6;
conf.mode = GPIO_MODE_INPUT;
GPIO_Init(&conf) ;
while (1) { }
}
<main>:
movs r3, #6
push {r0, r1, r2, lr}
str r3, [sp, #0]
mov r0, sp
subs r3, #5
str r3, [sp, #4]
bl 8000198 <GPIO_Init>
b.n 80001f4 <main+0x10>
prepare to pass the address of the GPIO_InitStruct
structure to the GPIO_Init function

## Slide 12
Inefficiencies in HAL
int main (void) {
GPIO_InitStruct conf = { 0 };
conf.pin = GPIO_PIN_6;
conf.mode = GPIO_MODE_INPUT;
GPIO_Init(&conf) ;
while (1) { }
}
<main>:
movs r3, #6
push {r0, r1, r2, lr}
str r3, [sp, #0]
mov r0, sp
subs r3, #5
str r3, [sp, #4]
bl 8000198 <GPIO_Init>
b.n 80001f4 <main+0x10>
set up the mode value for GPIO_MODE_INPUT (subtract 5 from 6 -> 1)

## Slide 13
Inefficiencies in HAL
int main (void) {
GPIO_InitStruct conf = { 0 };
conf.pin = GPIO_PIN_6;
conf.mode = GPIO_MODE_INPUT;
GPIO_Init(&conf) ;
while (1) { }
}
<main>:
movs r3, #6
push {r0, r1, r2, lr}
str r3, [sp, #0]
mov r0, sp
subs r3, #5
str r3, [sp, #4]
bl 8000198 <GPIO_Init>
b.n 80001f4 <main+0x10>
store the mode value in the GPIO_InitStruct structure on the stack

## Slide 14
Inefficiencies in HAL
int main (void) {
GPIO_InitStruct conf = { 0 };
conf.pin = GPIO_PIN_6;
conf.mode = GPIO_MODE_INPUT;
GPIO_Init(&conf) ;
while (1) { }
}
<main>:
movs r3, #6
push {r0, r1, r2, lr}
str r3, [sp, #0]
mov r0, sp
subs r3, #5
str r3, [sp, #4]
bl 8000198 <GPIO_Init>
b.n 80001f4 <main+0x10>
call the GPIO_Init function with the GPIO_InitStruct
structure as an argument

## Slide 15
Inefficiencies in HAL
int main (void) {
GPIO_InitStruct conf = { 0 };
conf.pin = GPIO_PIN_6;
conf.mode = GPIO_MODE_INPUT;
GPIO_Init(&conf) ;
while (1) { }
}
<main>:
movs r3, #6
push {r0, r1, r2, lr}
str r3, [sp, #0]
mov r0, sp
subs r3, #5
str r3, [sp, #4]
bl 8000198 <GPIO_Init>
b.n 80001f4 <main+0x10>
create an infinite loop (branch to the same address)

## Slide 16
Inefficiencies in HAL
typedef struct {
uint32_t pin;
GPIO_Modes mode;
} GPIO_InitStruct;
void GPIO_Init(GPIO_InitStruct* conf) {
uint32_t temp;
/* check the values */
if (!IS_GPIO_PIN(conf->pin)) { return; }
if (!IS_GPIO_MODE(conf->mode)) { return; }
/* configure the GPIO based on the settings */
if (conf->mode == GPIO_MODE_OUTPUT) {
temp = OSPEEDR;
temp &= ~(OSPEEDR_MASK << (conf->pin * 2u));
temp |= (GPIO_SPEED_FREQ_LOW << (conf->pin * 2u));
OSPEEDR = temp;
/* ... */
}
/* ... */
}
ldr r2, [r0, #0]
push {r4, r5, lr}
cmp r2, #15
bhi.n 80001da <GPIO_Init+0x42>
ldrb r3, [r0, #4]
cmp r3, #1
bhi.n 80001da <GPIO_Init+0x42>
bne.n 80001c4 <GPIO_Init+0x2c>
movs r4, #3
lsls r2, r2, #1
lsls r4, r2
ldr r5, [pc, #44]
ldr r1, [r5, #0]
bics r1, r4
movs r4, r3
str r1, [r5, #0]
if pin is greater than 15, branch to the end (invalid pin check)

## Slide 17
Inefficiencies in HAL
typedef struct {
uint32_t pin;
GPIO_Modes mode;
} GPIO_InitStruct;
void GPIO_Init(GPIO_InitStruct* conf) {
uint32_t temp;
/* check the values */
if (!IS_GPIO_PIN(conf->pin)) { return; }
if (!IS_GPIO_MODE(conf->mode)) { return; }
/* configure the GPIO based on the settings */
if (conf->mode == GPIO_MODE_OUTPUT) {
temp = OSPEEDR;
temp &= ~(OSPEEDR_MASK << (conf->pin * 2u));
temp |= (GPIO_SPEED_FREQ_LOW << (conf->pin * 2u));
OSPEEDR = temp;
/* ... */
}
/* ... */
}
ldr r2, [r0, #0]
push {r4, r5, lr}
cmp r2, #15
bhi.n 80001da <GPIO_Init+0x42>
ldrb r3, [r0, #4]
cmp r3, #1
bhi.n 80001da <GPIO_Init+0x42>
bne.n 80001c4 <GPIO_Init+0x2c>
movs r4, #3
lsls r2, r2, #1
lsls r4, r2
ldr r5, [pc, #44]
ldr r1, [r5, #0]
bics r1, r4
movs r4, r3
str r1, [r5, #0]
if mode is greater than 1, branch to the end (invalid mode check)

## Slide 18
Inefficiencies in HAL
typedef struct {
uint32_t pin;
GPIO_Modes mode;
} GPIO_InitStruct;
void GPIO_Init(GPIO_InitStruct* conf) {
uint32_t temp;
/* check the values */
if (!IS_GPIO_PIN(conf->pin)) { return; }
if (!IS_GPIO_MODE(conf->mode)) { return; }
/* configure the GPIO based on the settings */
if (conf->mode == GPIO_MODE_OUTPUT) {
temp = OSPEEDR;
temp &= ~(OSPEEDR_MASK << (conf->pin * 2u));
temp |= (GPIO_SPEED_FREQ_LOW << (conf->pin * 2u));
OSPEEDR = temp;
/* ... */
}
/* ... */
}
ldr r2, [r0, #0]
push {r4, r5, lr}
cmp r2, #15
bhi.n 80001da <GPIO_Init+0x42>
ldrb r3, [r0, #4]
cmp r3, #1
bhi.n 80001da <GPIO_Init+0x42>
bne.n 80001c4 <GPIO_Init+0x2c>
movs r4, #3
lsls r2, r2, #1
lsls r4, r2
ldr r5, [pc, #44]
ldr r1, [r5, #0]
bics r1, r4
movs r4, r3
str r1, [r5, #0]
if mode is not 1, branch to configure pin for input mode

## Slide 19
Inefficiencies in HAL
typedef struct {
uint32_t pin;
GPIO_Modes mode;
} GPIO_InitStruct;
void GPIO_Init(GPIO_InitStruct* conf) {
uint32_t temp;
/* check the values */
if (!IS_GPIO_PIN(conf->pin)) { return; }
if (!IS_GPIO_MODE(conf->mode)) { return; }
/* configure the GPIO based on the settings */
if (conf->mode == GPIO_MODE_OUTPUT) {
temp = OSPEEDR;
temp &= ~(OSPEEDR_MASK << (conf->pin * 2u));
temp |= (GPIO_SPEED_FREQ_LOW << (conf->pin * 2u));
OSPEEDR = temp;
/* ... */
}
/* ... */
}
ldr r2, [r0, #0]
push {r4, r5, lr}
cmp r2, #15
bhi.n 80001da <GPIO_Init+0x42>
ldrb r3, [r0, #4]
cmp r3, #1
bhi.n 80001da <GPIO_Init+0x42>
bne.n 80001c4 <GPIO_Init+0x2c>
movs r4, #3
lsls r2, r2, #1
lsls r4, r2
ldr r5, [pc, #44]
ldr r1, [r5, #0]
bics r1, r4
movs r4, r3
str r1, [r5, #0]
prepare mask value for OSPEEDR (3)

## Slide 20
Inefficiencies in HAL
typedef struct {
uint32_t pin;
GPIO_Modes mode;
} GPIO_InitStruct;
void GPIO_Init(GPIO_InitStruct* conf) {
uint32_t temp;
/* check the values */
if (!IS_GPIO_PIN(conf->pin)) { return; }
if (!IS_GPIO_MODE(conf->mode)) { return; }
/* configure the GPIO based on the settings */
if (conf->mode == GPIO_MODE_OUTPUT) {
temp = OSPEEDR;
temp &= ~(OSPEEDR_MASK << (conf->pin * 2u));
temp |= (GPIO_SPEED_FREQ_LOW << (conf->pin * 2u));
OSPEEDR = temp;
/* ... */
}
/* ... */
}
ldr r2, [r0, #0]
push {r4, r5, lr}
cmp r2, #15
bhi.n 80001da <GPIO_Init+0x42>
ldrb r3, [r0, #4]
cmp r3, #1
bhi.n 80001da <GPIO_Init+0x42>
bne.n 80001c4 <GPIO_Init+0x2c>
movs r4, #3
lsls r2, r2, #1
lsls r4, r2
ldr r5, [pc, #44]
ldr r1, [r5, #0]
bics r1, r4
movs r4, r3
str r1, [r5, #0]
shift pin value left by 1 bit (pin * 2)

## Slide 21
Inefficiencies in HAL
typedef struct {
uint32_t pin;
GPIO_Modes mode;
} GPIO_InitStruct;
void GPIO_Init(GPIO_InitStruct* conf) {
uint32_t temp;
/* check the values */
if (!IS_GPIO_PIN(conf->pin)) { return; }
if (!IS_GPIO_MODE(conf->mode)) { return; }
/* configure the GPIO based on the settings */
if (conf->mode == GPIO_MODE_OUTPUT) {
temp = OSPEEDR;
temp &= ~(OSPEEDR_MASK << (conf->pin * 2u));
temp |= (GPIO_SPEED_FREQ_LOW << (conf->pin * 2u));
OSPEEDR = temp;
/* ... */
}
/* ... */
}
ldr r2, [r0, #0]
push {r4, r5, lr}
cmp r2, #15
bhi.n 80001da <GPIO_Init+0x42>
ldrb r3, [r0, #4]
cmp r3, #1
bhi.n 80001da <GPIO_Init+0x42>
bne.n 80001c4 <GPIO_Init+0x2c>
movs r4, #3
lsls r2, r2, #1
lsls r4, r2
ldr r5, [pc, #44]
ldr r1, [r5, #0]
bics r1, r4
movs r4, r3
str r1, [r5, #0]
shift mask value left by (pin * 2) positions

## Slide 22
Inefficiencies in HAL
typedef struct {
uint32_t pin;
GPIO_Modes mode;
} GPIO_InitStruct;
void GPIO_Init(GPIO_InitStruct* conf) {
uint32_t temp;
/* check the values */
if (!IS_GPIO_PIN(conf->pin)) { return; }
if (!IS_GPIO_MODE(conf->mode)) { return; }
/* configure the GPIO based on the settings */
if (conf->mode == GPIO_MODE_OUTPUT) {
temp = OSPEEDR;
temp &= ~(OSPEEDR_MASK << (conf->pin * 2u));
temp |= (GPIO_SPEED_FREQ_LOW << (conf->pin * 2u));
OSPEEDR = temp;
/* ... */
}
/* ... */
}
ldr r2, [r0, #0]
push {r4, r5, lr}
cmp r2, #15
bhi.n 80001da <GPIO_Init+0x42>
ldrb r3, [r0, #4]
cmp r3, #1
bhi.n 80001da <GPIO_Init+0x42>
bne.n 80001c4 <GPIO_Init+0x2c>
movs r4, #3
lsls r2, r2, #1
lsls r4, r2
ldr r5, [pc, #44]
ldr r1, [r5, #0]
bics r1, r4
movs r4, r3
str r1, [r5, #0]
load address of OSPEEDR into r5

## Slide 23
Inefficiencies in HAL
typedef struct {
uint32_t pin;
GPIO_Modes mode;
} GPIO_InitStruct;
void GPIO_Init(GPIO_InitStruct* conf) {
uint32_t temp;
/* check the values */
if (!IS_GPIO_PIN(conf->pin)) { return; }
if (!IS_GPIO_MODE(conf->mode)) { return; }
/* configure the GPIO based on the settings */
if (conf->mode == GPIO_MODE_OUTPUT) {
temp = OSPEEDR;
temp &= ~(OSPEEDR_MASK << (conf->pin * 2u));
temp |= (GPIO_SPEED_FREQ_LOW << (conf->pin * 2u));
OSPEEDR = temp;
/* ... */
}
/* ... */
}
ldr r2, [r0, #0]
push {r4, r5, lr}
cmp r2, #15
bhi.n 80001da <GPIO_Init+0x42>
ldrb r3, [r0, #4]
cmp r3, #1
bhi.n 80001da <GPIO_Init+0x42>
bne.n 80001c4 <GPIO_Init+0x2c>
movs r4, #3
lsls r2, r2, #1
lsls r4, r2
ldr r5, [pc, #44]
ldr r1, [r5, #0]
bics r1, r4
movs r4, r3
str r1, [r5, #0]
load current OSPEEDR value into r1

## Slide 24
Inefficiencies in HAL
typedef struct {
uint32_t pin;
GPIO_Modes mode;
} GPIO_InitStruct;
void GPIO_Init(GPIO_InitStruct* conf) {
uint32_t temp;
/* check the values */
if (!IS_GPIO_PIN(conf->pin)) { return; }
if (!IS_GPIO_MODE(conf->mode)) { return; }
/* configure the GPIO based on the settings */
if (conf->mode == GPIO_MODE_OUTPUT) {
temp = OSPEEDR;
temp &= ~(OSPEEDR_MASK << (conf->pin * 2u));
temp |= (GPIO_SPEED_FREQ_LOW << (conf->pin * 2u));
OSPEEDR = temp;
/* ... */
}
/* ... */
}
ldr r2, [r0, #0]
push {r4, r5, lr}
cmp r2, #15
bhi.n 80001da <GPIO_Init+0x42>
ldrb r3, [r0, #4]
cmp r3, #1
bhi.n 80001da <GPIO_Init+0x42>
bne.n 80001c4 <GPIO_Init+0x2c>
movs r4, #3
lsls r2, r2, #1
lsls r4, r2
ldr r5, [pc, #44]
ldr r1, [r5, #0]
bics r1, r4
movs r4, r3
str r1, [r5, #0]
clear the two bits for the pin in OSPEEDR

## Slide 25
Inefficiencies in HAL
typedef struct {
uint32_t pin;
GPIO_Modes mode;
} GPIO_InitStruct;
void GPIO_Init(GPIO_InitStruct* conf) {
uint32_t temp;
/* check the values */
if (!IS_GPIO_PIN(conf->pin)) { return; }
if (!IS_GPIO_MODE(conf->mode)) { return; }
/* configure the GPIO based on the settings */
if (conf->mode == GPIO_MODE_OUTPUT) {
temp = OSPEEDR;
temp &= ~(OSPEEDR_MASK << (conf->pin * 2u));
temp |= (GPIO_SPEED_FREQ_LOW << (conf->pin * 2u));
OSPEEDR = temp;
/* ... */
}
/* ... */
}
ldr r2, [r0, #0]
push {r4, r5, lr}
cmp r2, #15
bhi.n 80001da <GPIO_Init+0x42>
ldrb r3, [r0, #4]
cmp r3, #1
bhi.n 80001da <GPIO_Init+0x42>
bne.n 80001c4 <GPIO_Init+0x2c>
movs r4, #3
lsls r2, r2, #1
lsls r4, r2
ldr r5, [pc, #44]
ldr r1, [r5, #0]
bics r1, r4
movs r4, r3
str r1, [r5, #0]
GPIO_SPEED_FREQ_LOW is 0 -> optimized

## Slide 26
Inefficiencies in HAL
typedef struct {
uint32_t pin;
GPIO_Modes mode;
} GPIO_InitStruct;
void GPIO_Init(GPIO_InitStruct* conf) {
uint32_t temp;
/* check the values */
if (!IS_GPIO_PIN(conf->pin)) { return; }
if (!IS_GPIO_MODE(conf->mode)) { return; }
/* configure the GPIO based on the settings */
if (conf->mode == GPIO_MODE_OUTPUT) {
temp = OSPEEDR;
temp &= ~(OSPEEDR_MASK << (conf->pin * 2u));
temp |= (GPIO_SPEED_FREQ_LOW << (conf->pin * 2u));
OSPEEDR = temp;
/* ... */
}
/* ... */
}
ldr r2, [r0, #0]
push {r4, r5, lr}
cmp r2, #15
bhi.n 80001da <GPIO_Init+0x42>
ldrb r3, [r0, #4]
cmp r3, #1
bhi.n 80001da <GPIO_Init+0x42>
bne.n 80001c4 <GPIO_Init+0x2c>
movs r4, #3
lsls r2, r2, #1
lsls r4, r2
ldr r5, [pc, #44]
ldr r1, [r5, #0]
bics r1, r4
movs r4, r3
str r1, [r5, #0]
store the modified OSPEEDR value back

## Slide 27
Runtime bitmask calculations
Runtime branching
Function calls
Runtime input validation
Inefficiencies in HAL

## Slide 28
Runtime bitmask calculations
Runtime branching
Function calls
Runtime input validation
Inefficiencies in HAL

## Slide 29
Encapsulation

## Slide 30
Inheritance

## Slide 31
Dynamic Polymorphism

## Slide 32
Static Polymorphism

## Slide 33
This is about the “special” cases where the hardware is known, which is common for embedded systems.
I did not replace the HAL given by the manufacturer, I extended it.
The same techniques can be used in any other application as well, if the circumstances allow it.
These are no guidelines or rules.
Notes

## Slide 34
Enumerations
enum class modes : std::uint32_t {
input = 0b00,
output = 0b01,
alt_func = 0b10,
analog = 0b11
};
enum class ports : std::uint8_t {
port_f,
port_d,
port_c,
port_b,
port_a
};
Enumerations
  Not plain integers anymore
  No implicit conversions between enum values and integral types
      Explicit static_cast required
      Harder to misuse accidentally

## Slide 35
Concepts
template <modes mode>
concept is_valid_mode = (
(mode == modes::input) ||
(mode == modes::output) ||
(mode == modes::alt_func) ||
(mode == modes::analog)
);
template <pins pin>
concept is_valid_pin = (
is_valid_low_pin<pin> || is_valid_high_pin<pin>
);
template <pins... pin>
concept are_valid_pins = (is_valid_pin<pin> && ...);

## Slide 36
Immediate Functions
template <modes mode, pins... pin>
requires (are_valid_pins<pin ...> && is_valid_mode<mode>)
consteval std::uint32_t moder_value () {
return (... | (static_cast<std::uint32_t>(mode) <<
(static_cast<std::uint32_t>(pin) * 2)));
}
template <pins... pin>
requires (are_valid_pins<pin ...>)
consteval std::uint32_t moder_bitmask () {
return (... | (GPIO_MODER_MODER0 <<
(static_cast<std::uint32_t>(pin) * 2)));
}

## Slide 37
Compile-time Branching

## Slide 38
Measurement